## Slide 1
LiDAR Ray Tracing for GNSS NLOS Detection
Use the 3D point cloud as the “city” to tell whether each satellite signal is direct or blocked
UrbanNav HK Medium-Urban-1 · West Kowloon, Hong Kong · 2021-05-17 · ~657 epochs

## Slide 2
The problem: in urban canyons, buildings block satellite signals
2 / 13
• In dense high-rise areas, many satellite signals cannot reach the receiver directly
• A blocked signal arrives only after reflecting off a wall — this is called NLOS (non-line-of-sight)
• Reflection adds extra travel distance → pseudorange too long → positioning error of tens of metres
Building
Building
Receiver
Sat A
Direct (LOS)
Sat B
✗ blocked
reflected (NLOS) extra path ΔL

## Slide 3
Core idea: ray-trace each satellite through a LiDAR map
3 / 13
• The 3D point cloud from LiDAR is a precise model of the city (every building included)
• From the receiver, draw a straight line (a ray) toward each satellite
• Ray reaches the sky unobstructed → LOS (direct); ray hits a building → NLOS (blocked)
• Pure geometry — no training data needed, fast and fully explainable
• Payoff: knowing which satellites are unreliable lets us treat them differently when positioning

## Slide 4
The full pipeline: five steps
4 / 13
1
LiDAR point-cloud map
2
Satellite directions (az / el)
3
Ray casting LOS / NLOS
4
Reflection geometry estimate ΔL
5
Feed into positioning
This talk focuses on the middle three steps (red/orange): how ray tracing finds NLOS and estimates the extra path.

## Slide 5
Step 1: turn the point cloud into a voxel world
5 / 13
• A voxel = a 0.5 m cube of space; a cube containing points = a building is there
• Ground points are filtered out (keep only what is above the receiver) to avoid false hits
• The ray only needs to ask “is this cube occupied?”, which is extremely fast
8,531,577
total cloud points
2,860,032
after ground filter
0.5 m
voxel size
1,333,519
occupied voxels

## Slide 6
Step 2: compute where each satellite is in the sky
6 / 13
• For every epoch and satellite, compute azimuth + elevation (its position in the sky)
• Three constellations together: GPS + BeiDou + Galileo
• More constellations → more visible satellites → better geometry → more robust positioning
5.8
GPS sats/epoch
6.4
BeiDou sats/epoch
3.8
Galileo sats/epoch
15.9
avg total/epoch

## Slide 7
Step 3: cast the ray and check voxel by voxel
7 / 13
• Step 0.5 m along the satellite direction, test each cube; a hit within 80 m → NLOS, otherwise LOS
Building
Receiver
Satellite
✗ hits building → NLOS
Step 0.5 m at a time, check each voxel for a building
Throughput: 14,773 rays/s (~1 s total)

## Slide 8
Result: more than half of all satellites are NLOS
8 / 13
Chart: 
| LOS | NLOS
s | 4472 | 6578
• Total 11,050 satellite×epoch records
• NLOS: 6,578 = 59.5%
• ~9.5 of the 15.9 visible satellites per epoch are blocked
• Using all pseudoranges blindly is bound to suffer heavy multipath

## Slide 9
Going further: modelling double reflections (2-bounce)
9 / 13
• After a hit, estimate the wall orientation (normal via PCA) and trace on along the mirror-reflection direction to a second wall
Building
Building
Receiver
Satellite
d1
d2
Two bounces: wall 1 (d1) → reflect → wall 2 (d2) → receiver, total extra path ≈ d1 + d2

## Slide 10
Quantifying the extra path: reflection geometry ΔL
10 / 13
ΔL = 2 · d · cos θ
• d = distance to the wall, θ = incidence angle (from the normal)
• ΔL = how much further the signal travels than a straight line
2,753
NLOS modelled
6.70 m
mean ΔL
6.45 m
median ΔL
54.6°
mean incidence
Chart: 
| Mild <2m | Strong 2-10m | Severe ≥10m
ΔL | 402 | 1868 | 483
Multipath severity: most NLOS are “strong” (glass facades), ~6.7 m on average

## Slide 11
What it is for: give ΔL back to positioning
11 / 13
• Subtract ΔL from the NLOS pseudorange to correct multipath; unreliable ones can be down-weighted or removed
• Three positioning modes compared (mean horizontal error):
Chart: 
| Baseline | Exclusion | Correction
m | 26.45 | 99 | 39.97
• Removing all NLOS starves geometry — worse (99 m)
• Correction is 39.97 m, not yet beating baseline 26.45 m
• Why? See next slide

## Slide 12
Current limits & next steps
12 / 13
Limitations
• Only 42% of NLOS modelled (3,825 skipped due to timestamp mismatch)
• 41% of surfaces are corners/curved — unreliable normals, ΔL off by 5–15 m
• Correction is applied bluntly, with no confidence weighting
Next steps
• Fix timestamp/leap-second alignment → coverage 42% → >85%
• Confidence-weighted “soft” correction (trust flat surfaces more)
• Add fault detection (FDE / RAIM) to drop missed large-error satellites
• Goal: push correction RMS below 20–25 m to truly beat baseline

## Slide 13
One-slide summary
• End-to-end ray-tracing pipeline: LiDAR map → sat directions → LOS/NLOS → reflection ΔL → positioning
• Quantified the urban-canyon NLOS rate: 59.5% (6,578 of 11,050)
• Geometrically modelled multipath: mean ΔL 6.7 m, explainable, 14,773 rays/s
• Multi-constellation baseline reaches 26.45 m — already good for an urban canyon
• Next: make the correction a net win (coverage + confidence weighting + FDE)